## Slide 1
Level 0
Physical Process
Field I/O device
IIoT
Metering Unit
Sensors
Level 1
Controller LAN
PLC
RTU
Level 2
Control Center (HQ) Processing LAN
MQTT Broker Server
Railway Track Control HMI
Control HMI / Console machine
Level 3
Operations Management Zone
Control Touch Screen/Phone
Monitor Desktop
MQTT Communication Channel
MQTT Client
MQTT Client
MQTT Client
Provide The MQTT Client connection interface lib to publish the data to the broker server
Provide The MQTT Client connection interface lib to subscribe the data from the broker server
Provide The MQTT Broker interface lib to save the data execution the control logic and handle all the data publish and subscribe request
Different OT levels MQTT data follow with related Broker server and Client device configuration

## Slide 3
IIoT Drone Simulator program
Air Vacuum System Control RTU Simulation Framework
Level1 OT Controller Devices
Input Parameter Dict
Level0 OT Physical Field I/O Devices
Auto
Control
Logic
Level2 OT Control Console/HMI/
Output Parameter Dict
MQTT Client
Smart Factory Air Vacuum System
UDP Simulated Electrical Signal RTU Input
UDP Simulated Electrical Signal RTU Output
IoT 5G Antenna
MQTT Client
MQTT Broker
Data Process Logic
Data Publish (Drone fly data)
Data Publish ( temp and fan-speed data)
Data Subscribe (Fan and valve moto control request )
MQTT Client
Drone State Monitor HMI
MQTT Client
Level3 OT Data Center
Factory Environment Monitor Dashboard
MQTT Data Subscribe Request
MQTT Data Publish Request
MQTT Broker
Data Publish ( Direct Overwrite control